## Slide 1: Packet-Loss-Feedback: An Effective Way to Improve Energy Efficiency for Long Concurrent Transmission
Qiang Li
Advisor: Omprakash Gnawali
11/09/2014

## Slide 2: Outline
Introduction
Previous Work: CXFS Protocol
Packet-loss-feedback(PLF)
Evaluation of 3 Variants of PLF
Conclusion
Future Work

## Slide 3: Outline
Introduction
Previous Work: CXFS Protocol
Packet-loss-feedback(PLF)
Evaluation of 3 Variants of PLF
Conclusion
Future Work

## Slide 4: Introduction
Traditional Way for Wireless Communication
  Conflict Avoid/Detection
  Keep Status
Concurrent Transmission
  Constructive Interference
  Flooding (No status)
  Example: Glossy Flooding

## Slide 5: Introduction
Why Concurrent Transmission?
  Pros
    Reliable
    No need to keep status
  Cons
    Synchronization
    Energy consumption
Problem: How to lower down power consumption?

## Slide 6: Outline
Introduction
Previous Work: CXFS Protocol
Packet-loss-feedback(PLF)
Evaluation of 3 Variants of PLF
Conclusion
Future Work

## Slide 7: CXFS Protocol: Basic Concepts
Time Slot and Frame
Three Basic Roles
  Master, slot owner, leaf node
Basic Idea: Reduce Forwarder Set Size
  Use hop-count as metric
  Use triangle Inequity to determine if a mote should forward or sleep

## Slide 8: CXFS Protocol: Basic Idea
Master
Slot Owner
Leaf
SI
ID
SD
Master
Slot Owner
Leaf
SI
ID
SD
Forwarding Criteria: SI + ID <= SD + tolerance
Case 1
Case 2
X
X

## Slide 9: CXFS Protocol
Restriction
  Hop-count not stable
  Tolerance
Still unnecessary forwarding nodes

## Slide 10: Outline
Introduction
Previous Work: CXFS Protocol
Packet-loss-feedback(PLF)
Evaluation of 3 Variants of PLF
Conclusion
Future Work

## Slide 11: PLF: Basic Idea
Inspired by TCP flow/congestion control
Protocol based on CXFS
  Generate Forwarder Set using CXFS algorithm
2-Phase-Optimization to Reduce CXFS Forwarder Set Size
  Leave Phase
    After forwarding a data packet, each forwarder will try to leave forwarder set randomly with a specific probability until packet loss happens;
  Return Phase
    Motes who left forwarder set check if their leave is related with packet loss. If yes, the motes should return to forwarder set, vice versa.
For each stream (master, slot owner), only one 2-Phase-Optimization

## Slide 12: PLF: Design Tradeoff
Improve Energy Efficiency at the expense of PRR
  Intentionally introduce packet loss;
  Smaller forwarder set is more vulnerable to network dynamic/interference;
Stream must be long enough
  The optimization cost is independent with stream length;
  The longer stream is, the lower the relative cost

## Slide 13: PLF: 3 Variants
Variant 1(PLF-Win1): window size = 1
  A mote will return to forwarder set if the packet sent from slot owner immediately after its leave is lost; otherwise it will leave permanently;
Variant 2(PLF-Win5-I): window size = 5
  If PRR of 5 consecutive packets sent immediately after a mote leaves the forwarder set is lower than a threshold (60%), this mote will return to forwarder set;
Variant 3(PLF-Win5-G): window size = 5
  If there is a packet loss happened in window, this mote will return; and if PRR of this window is lower than a threshold, all motes will act as CXFS motes in the remaining stream;

## Slide 14: PLF: Purpose of 3 Variants
Aggressiveness in Energy Conservation
  PLF-Win1 > PLF-Win5-I > PLF-Win5-G
  High PRR oriented
  PLF-Win1 > PLF-Win5-I > PLF-Win5-G

## Slide 15: Outline
Introduction
Previous Work: CXFS Protocol
Packet-loss-feedback(PLF)
Evaluation of 3 Variants of PLF
Conclusion
Future Work

## Slide 16: Evaluation
Testbed: consist of 27 Bacon Motes, deployed in an Academic Building

## Slide 17: Evaluation
Experiment Settings
  Set mote 0 as Master;
  Each mote will send 100 packets to Master;
  Each slot consists of 80 frames;
  Forwarder randomly leave forwarder set at Probability = 30%;
  Transmission Power –6 dBm;
  For each variant we run 3 rounds and take the average;
  We tried to run experiments at same time slot;

## Slide 18: Evaluation: PRR of Each Mote
Average PRR of Each Mote
Aggregate PRR for each setting

## Slide 19: Evaluation: Forwarder Set Size(I)
Typical near-end mote

## Slide 20: Evaluation: Forwarder Set Size(II)
Typical far-end mote

## Slide 21: Evaluation: Duty Cycle
Duty Cycle of a typical mote
Duty Cycle of a typical mote across all slots

## Slide 22: Evaluation: Overall Comparison

## Slide 23: Outline
Introduction
Previous Work: CXFS Protocol
Packet-loss-feedback(PLF)
Evaluation of 3 Variants of PLF
Conclusion
Future Work

## Slide 24: Conclusion
PLF reduces duty cycle of the whole network significantly at reasonable expense of PRR;
PLF-Win1 is most aggressive in energy conservation, but is more vulnerable to network dynamic;
PLF-Win5-I and PLF-Win5-G are more balanced in energy consumption and acceptable PRR.

## Slide 25: Outline
Introduction
Previous Work: CXFS Protocol
Packet-loss-feedback(PLF)
Evaluation of 3 Variants of PLF
Conclusion
Future Work

## Slide 26: Future Work
How different probability(for example, 15%) will affect duty cycle and PRR?
Implement PLF on other testbed to make sure these results are platform/topology independent;

## Slide 27: Other Work
Paper:
1. “ On the Effectiveness of Energy Metering on Every Node ” by Qiang Li, Marcelo Martins, Omprakash Gnawali, and Rodrigo Fonseca. In Proceedings of the 9th International Conference on Distributed Computing in Sensor Systems (DCOSS 2013) , May 2013.
Demo:
1. “ Demo Abstract: Twonet - Large-Scale Wireless Sensor Network Testbed with Dual-Radio Nodes ” by Qiang Li, Dong Han, Omprakash Gnawali, Philipp Sommer and Branislav Kusyand. In ACM Conference on Embedded Networked Sensor Systems (SenSys 2013) , November 2013.

## Slide 28: Reference
[1] F. Ferrari, M. Zimmerling, L. Mottola, and L. Thiele. Low-power wireless bus. In 10th ACM Conf. on Embedded Networked Sensor Systems (SenSys 12), 2012.
[2] F. Ferrari, M. Zimmerling, L. Thiele, and O. Saukh. Efficient network flooding and time synchronization with glossy. In Proceedings of the 10th International Conference on Information Processing in Sensor Networks (IPSN), Chicago, IL, USA, 2011. ACM/IEEE.
[3] F. Osterlind, L. Mottola, T. Voigt, N. Tsiftes, and A. Dunkels. Straw-man: resolving collisions in bursty low-power wireless networks. In Proceedings of the 11th international conference on Information Processing in Sensor Networks, pages 161–172. ACM, 2012.
[4] D. Son, B. Krishnamachari, and J. Heidemann. Experimental study of concurrent transmission in wireless sensor networks. In Proceedings of the ACM Sensys, Nov.2006. [5] Doug Carlson, Marcus Chang, Yin Chen, Andreas Terzis, Omprakash Gnawali. Forwarder Selection in Multi-Transmitter Networks, In Proceedings at DCOSS 2013, Cambridge, MA USA.